Aeronautical Mobile Radio Interface Specifications

Contact Information

Spektrum Yönetimi Dairesi Başkanlığı

Bilgi Teknolojileri ve İletişim Kurumu

Eskişehir Yolu 10. km. No:276 Çankaya / Ankara

Tel		: +90 312 294 7310

E-posta	: MFP@btk.gov.tr

Web		: www.btk.gov.tr

List of Aeronautical Mobile Radio Interface Specifications

| Reference Number | Service | Application | Frequency Band | Comment |
| --- | --- | --- | --- | --- |
| TAD-05-01-01 | Aeronautical Mobile | AGA communications | 117.975 - 137.000 MHz | VHF Communication |
| TAD-05-01-02 | Aeronautical Mobile | AGA communications | 108 - 117.95 MHz 117.975 - 137.000 MHz | VDL Mode 2- VDL Mode 4 |
| TAD-05-01-03 | Aeronautical Mobile | AGA communications | 2850–3025 kHz 3400–3500 kHz 4650–4700 kHz 5480–5680 kHz 6525–6685 kHz 8815–8965 kHz 10005–10100 kHz 11275–11400 kHz 13260–13360 kHz 17900–17970 kHz 21924–22000 kHz | HF SSB airborne radio equipment for voice and data communication |
| TAD-05-02-01 | Aeronautical Radionavigation | Beacons (aeronautical) | 255.0 - 526.5 kHz | NDB |
| TAD-05-02-02 | Aeronautical Radionavigation | VOR | 108.000 - 117.975 MHz | VOR / DVOR |
| TAD-05-02-03 | Aeronautical Radionavigation | GBAS | 108-117.975 MHz | GBAS |
| TAD-05-02-04 | Aeronautical Radionavigation | DME | 960 - 1215 MHz | DME |
| TAD-05-02-05 | Aeronautical Radionavigation | ILS | 108 - 117.975 MHz 328.6 - 335.4 MHz | Localizer and Glidepath |
| TAD-05-02-06 | Aeronautical Radionavigation | Beacons (aeronautical) | 74.800 - 75.200 MHz | Marker |
| TAD-05-03-01 | Aeronautical Radionavigation | Primary Radar | 1300 - 1350 MHz 2700 - 2900 MHz 9000 - 9200 MHz | PSR |
| TAD-05-03-02 | Aeronautical Radionavigation | SSR | 960 - 1164 MHz | SSR |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Air Ground Air communications | TAD05-01-01 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical Mobile | VHF Communication |
|  | 2 | Application | Air Ground Air communications | Voice Communication, VHF COM 8.33 / 25 kHz / Data Communication (ACARS) |
|  | 3 | Frequency band | A: 117.975 - 137.000 MHz B: 121.5 MHz | 121.500 MHz (Band B) only for emergency. |
|  | 4 | Channelling | 8. 33 kHz/25 kHz |  |
|  | 5 | Modulation / Occupied bandwidth | A3E Analog voice: 25 kHz 6K80A3EJN and 8.33 kHz 5K00A3EJN, ACARS data link: 25 kHz 13K0A2DAN. In accordance with ICAO Annex 10 (Ref 1.1), as relevant. | ACARS: MSK (Minimum Shift Keying Modulation) 2400 bps ACARS (Aircraft Communications Addressing and Reporting System) |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 250 W transmitter power For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). | DOC -Designated operational coverage |
|  | 8 | Channel access and occupation rules | Data Link: ACARS uses CSMA protocol. In accordance with ICAO Annex 10 (Ref 1.1), as relevant. | CSMA – Carrier Sense Multiple Access |
|  | 9 | Authorisation regime | Subject to authorisation by BTK and radio operator certificate, radio license and permission to install and use the radio equipment by General Directorate of Coastal Safety | - |
|  | 10 | Additional essential requirements |  | - |
|  | 11 | Frequency planning assumptions | ICAO Annex 10 Volume III ICAO Annex 10 Volume V | Vertical |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 300 676, EN 301 489-22, ICAO Annex 10/Volume III, Volume V |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | AGA communications | TAD05-01-02 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical Mobile | VDL Mode 2- VDL Mode 4 |
|  | 2 | Application | AGA communications | VHF digital link, VDL Mode 2-VDL-Mode 4 |
|  | 3 | Frequency band | 108-117.95 MHz 117.975 - 137.000 MHz | 136.975 MHz CSC (Common Signalling Channel) |
|  | 4 | Channelling | 25 kHz (Mode 2) 25 kHz (Mode 4) |  |
|  | 5 | Modulation / Occupied bandwidth | Mode 2 Data Link 25 kHz 14K0G1D Mode 4 Data Link 25 kHz 13K0F7D | ICAO Annex 10 |
|  | 6 | Direction / Separation |  | - |
|  | 7 | Transmit power / Power density | Maximum 250 W transmitter power For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). |  |
|  | 8 | Channel access and occupation rules | Mode 2 CSMA (Carrier Sense Multiple Access), Mode 4 STDMA (Self-Organising Time Division Multiple Access) | ICAO Annex 10 |
|  | 9 | Authorisation regime | Subject to radio operator certificate, radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety) | - |
|  | 10 | Additional essential requirements | - |  |
|  | 11 | Frequency planning assumptions | ICAO Annex 10 Volume V | Vertical |
| Informative Part | 12 | Planned changes | - |  |
|  | 13 | Reference | Mode 2: EN 301 841-1 Mode 4: EN 301 842-1 |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | AGA communications SAR (Search and Rescue) communications | TAD05-01-03 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical Mobile |  |
|  | 2 | Application | AGA communications SAR (Search and Rescue) communications |  |
|  | 3 | Frequency band | 2850–3025 kHz, 3400–3500 kHz, 4650–4700 kHz, 5480–5680 kHz, 6525–6685 kHz, 8815–8965 kHz, 10005–10100 kHz, 11275–11400 kHz, 13260–13360 kHz, 17900–17970 kHz, 21924–22000 kHz |  |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth | Analog Voice: 2K80J3EJN; HF data Link (HFDL): 2K80J2DEN; SELCAL (Selective Calling): 1K48H2BFN (Highest AudioTonu 1479.1 Hz). F1B, J7B ve J9B can also permitted. The frequencies 3023 MHz and 5680 MHz are used for search and rescue , with class of emission J3E. A3E and H3E classes of emission may also be used where maritime and land mobile services are involved. Sideband transmitted is on the higher side of the carrier (reference) frequency (Upper Sideband – USB). The carrier (reference) frequency is 1.4 kHz below the assigned frequency. The carrier (reference) frequencies are on multiples of 1 kHz separated by 3 kHz. The HFDL M-PSK1 carrier is offset from the SSB carrier (reference) frequency by 1.440 kHz. In accordance with ICAO Annex 10 (Ref 1.1), as relevant | ICAO Annex10 |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 6 kW p.e. p. Maximum 1.5 kW p.e. p for F1B |  |
|  | 8 | Channel access and occupation rules | Analog Voice: SELCAL Data Link: HFDL, TDMA | ICAO Annex10 |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - |  |
|  | 11 | Frequency planning assumptions | ICAO Annex 10 Volume 5, ITU-RR Appendix 27, CEPT / ERO Rec.74-01 |  |
| Informative Part | 12 | Planned changes | - |  |
|  | 13 | Reference | ICAO Annex 10 Volume 3 |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Beacons (aeronautical) | TAD05-02-01 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation |  |
|  | 2 | Application | Beacons (aeronautical) | NDB - Non Directional Beacons |
|  | 3 | Frequency band | 255.0 - 526.5 kHz |  |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth | Long transmission using Morse code (850HA2AAN) |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | According ICAO Annex 10 Volume I Chapter 3.4 |  |
|  | 8 | Channel access and occupation rules | According ICAO Annex 10 |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | 2005/53/EC |  |
|  | 11 | Frequency planning assumptions | ICAO Annex 10 Volume I ve Volume V | Vertical |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | ICAO Annex 10, Volume I, chapter 3.4 |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | VOR / DVOR | TAD05-02-02 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical Radionavigation |  |
|  | 2 | Application | VOR / DVOR | VOR - VHF Omnidirectional Radio Range DVOR - Doppler VOR |
|  | 3 | Frequency band | A: 111.975 - 117.975 MHz B: 108.000 - 111.975 MHz |  |
|  | 4 | Channelling | 50 kHz |  |
|  | 5 | Modulation / Occupied bandwidth | AM, FM / 20K9A9W | ICAO Annex 10 |
|  | 6 | Direction / Separation | - |  |
|  | 7 | Transmit power / Power density | ICAO Annex 10, Volume I, Chapter 3.3 For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety) | - |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions | Horizontal polarisation. |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 301 489-22, ICAO Annex 10, Volume I ve Volume V |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Aeronautical radionavigation | TAD05-02-03 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation |  |
|  | 2 | Application | GBAS | Ground based augmentation systems |
|  | 3 | Frequency band | 108 – 117.975 MHz |  |
|  | 4 | Channelling | 25 kHz |  |
|  | 5 | Modulation / Occupied bandwidth | 14K0G7DET (D8PSK). |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 25 kW transmitter power Maksimum 50 MW e.i.r.p. |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions |  |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | ICAO Annex 10 Volume 1 |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | DME | TAD-05-02-04 |  |
| --- | --- | --- | --- | --- |
|  | Nr | Parameter | Parameter | Description |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation | - |
|  | 2 | Application | DME | DME (Distance Measurement Equipment), TACAN (Tactical Air Navigation) |
|  | 3 | Frequency band | 960 - 1215 MHz |  |
|  | 4 | Channelling | 1 MHz | - |
|  | 5 | Modulation / Occupied bandwidth | - | ICAO Annex 10 |
|  | 6 | Direction / Separation | 63 MHz | - |
|  | 7 | Transmit power / Power density | ICAO Annex 10, Volume I, Chapter 3.3 For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). |  |
|  | 8 | Channel access and occupation rules |  | ICAO Annex 10 |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - | - |
|  | 11 | Frequency planning assumptions | ICAO Annex 10, Volume I ve Volume V | Vertical |
| Informative Part | 12 | Planned changes | - | - |
|  | 13 | Reference | ICAO Annex 10, Volume I ve Volume V |  |
|  | 14 | Notification number | - | - |
|  | 15 | Remarks |  | - |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | ILS | TAD-05-02-05 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Parameter | Description |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation | - |
|  | 2 | Application | ILS | ILS (Instrument Landing System) / Localizer and Glidepath ground station |
|  | 3 | Frequency band | A: 108–117.975 MHz B: 328.6–335.4 MHz | 108-117.975 MHz (Localizer) 328.6-335.4 MHz (Glidepath) |
|  | 4 | Channelling | A: 50 kHz B: 150 kHz | ICAO Annex 10 and ICAO Doc. 7754 |
|  | 5 | Modulation / Occupied bandwidth | Localizer: 2K04A7W (1 carrier without voice) , 16K0A7WA (2 carriers without voice). Glidepath: 300HA7N, 32K3A7N (two carriers) Amplutude Modulation | ICAO Annex 10 |
|  | 6 | Direction / Separation | - | - |
|  | 7 | Transmit power / Power density | For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). | ICAO Annex 10, Volume I, Chapter 3 |
|  | 8 | Channel access and occupation rules | - | - |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - | - |
|  | 11 | Frequency planning assumptions | Horizontal polarisation. | ICAO Annex 10, Volume I and Volume V |
| Informative Part | 12 | Planned changes | - | - |
|  | 13 | Reference | ICAO Annex 10, Volume I ve Volume V |  |
|  | 14 | Notification number |  | - |
|  | 15 | Remarks |  | - |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Beacons (aeronautical) | TAD-05-02-06 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Parameter | Description |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation | - |
|  | 2 | Application | Beacons (aeronautical) | Marker |
|  | 3 | Frequency band | 74.800 - 75.200 MHz |  |
|  | 4 | Channelling | - | - |
|  | 5 | Modulation / Occupied bandwidth | 800HA2A (Outer Marker (OM1)), 2K60A2A (Middle Marker (MM2)), 6K00A2A* (Inner Marker (IM3)). | ICAO Annex 10 |
|  | 6 | Direction / Separation | - | - |
|  | 7 | Transmit power / Power density | For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). | ICAO Annex 10, Volume I, Chapter 3.1 / 3.6 |
|  | 8 | Channel access and occupation rules | Markers will work with each other using the same frequency. | ICAO Annex 10 |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - | - |
|  | 11 | Frequency planning assumptions | Horizontal polarisation. | ICAO Annex 10, Volume I |
| Informative Part | 12 | Planned changes | - | - |
|  | 13 | Reference | ICAO Annex 10, Volume I |  |
|  | 14 | Notification number | - | - |
|  | 15 | Remarks |  | - |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Primary Radar | TAD-05-03-01 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Parameter | Description |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation | - |
|  | 2 | Application | Primary Radar | PSR - Primary Surveillance Radar ( ground based) |
|  | 3 | Frequency band | 1215 - 1350 MHz, 2700 - 3100 MHz, 9200 - 9500 MHz, 15.4 - 15.7 GHz | - |
|  | 4 | Channelling | - | - |
|  | 5 | Modulation / Occupied bandwidth | P0N , G0N | Pulse and Phase modulation |
|  | 6 | Direction / Separation | - | - |
|  | 7 | Transmit power / Power density | For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power (e.r.p.). |  |
|  | 8 | Channel access and occupation rules | - | - |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - | - |
|  | 11 | Frequency planning assumptions | ITU-RR Appendix 3 | ITU-R M.1177 (unwanted radar emissions), ITU-R SM.329-10 ((Unwanted emissions in the spurious domain), ITU-R SM.1541 (Unwanted emissions in the out-of-band domain), ERC/REC 74-01 |
| Informative Part | 12 | Planned changes | - | - |
|  | 13 | Reference | ERC/REC 74-01, ECC/REC/(02)05 |  |
|  | 14 | Notification number |  | - |
|  | 15 | Remarks |  | - |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | SSR | TAD-05-03-02 |  |
| --- | --- | --- | --- | --- |
|  |  | Nr | Parameter | Description |
| Normative Part | 1 | Radiocommunication Service | Aeronautical radionavigation | - |
|  | 2 | Application | SSR | Monopulse Secondary Surveillance Radar |
|  | 3 | Frequency band | 1030 MHz (Tx), 1090 MHz (Rx) |  |
|  | 4 | Channelling | 60 MHz | - |
|  | 5 | Modulation / Occupied bandwidth | L9D / M9D | ICAO Annex 10, Volume IV (ICAO Annex 10, Volume IV, Figure 3.2) |
|  | 6 | Direction / Separation | duplex |  |
|  | 7 | Transmit power / Power density | For each individual frequency assignment, either the maximum and minimum field strength at the limit of DOC may be specified or the maximum effective radiated power | ICAO Annex 10, Volume IV |
|  | 8 | Channel access and occupation rules |  | ICAO Annex 10 |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). | - |
|  | 10 | Additional essential requirements | - | - |
|  | 11 | Frequency planning assumptions | Vertical polarization. | ICAO Annex 10, Volume IV |
| Informative Part | 12 | Planned changes | - | - |
|  | 13 | Reference | ICAO Annex 10, Volume IV |  |
|  | 14 | Notification number |  | - |
|  | 15 | Remarks |  |  |