Maritime Mobile Radio Interface Specifications

Contact Information

Spektrum Yönetimi Dairesi Başkanlığı

Bilgi Teknolojileri ve İletişim Kurumu

Eskişehir Yolu 10. km. No:276 Çankaya / Ankara

Tel		: +90 312 294 7310

E-posta	: MFP@btk.gov.tr

Web		: www.btk.gov.tr

List of Maritime Mobile Radio Interface Specifications

| Reference Number | Service | Application | Frequency Band | Comment |
| --- | --- | --- | --- | --- |
| TAD06-01-01 | Maritime Mobile | GMDSS | 156 - 174 MHz | DSC VHF Radio |
| TAD06-01-02 | Maritime Mobile | GMDSS | 1605 - 27500 kHz | DSC MF/HF Radio |
| TAD06-01-03 | Mobile-Sattelite | EPIRBs | A: 121.45 - 121.55 MHz B: 242.95 - 243.05 MHz C: 406.00 - 406.10 MHz | GMDSS /COSPAS-SARSAT (121.5 MHz, 243 MHz / 406 MHz) |
| TAD06-01-04 | Maritime Mobile | AIS | 161.9625-161.9875 MHz 162.0125-162.0375 MHz | Automatic Identification System |
| TAD06-01-05 | Maritime | Maritime Radar | 9300 - 9500 MHz | Maritime Radar |
| TAD06-01-06 | Maritime | Maritime Radar | 9300 - 9500 MHz | Maritime Radar (non-SOLAS) |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | GMDSS | TAD06-01-01 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime Mobile |  |
|  | 2 | Application | GMDSS | DSC-capable VHF radiotelephone equipment |
|  | 3 | Frequency band | 156 - 174 MHz |  |
|  | 4 | Channelling | 12.5 kHz, 25 kHz |  |
|  | 5 | Modulation / Occupied bandwidth | G2B, G3E |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 25 W |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to GMDSS radio operator certificate, radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements | EN 300 162, EN 301 025 |  |
|  | 11 | Frequency planning assumptions |  |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 300 338, SOLAS, ITU-R, IMO, EN 301 843-1 (EMC), EN 301 843-2 (EMC), EN 62368-1 (LVD) |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | GMDSS | TAD06-01-02 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime Mobile |  |
|  | 2 | Application | GMDSS | DSC-capable VHF radiotelephone equipment |
|  | 3 | Frequency band | 1605-27500 kHz |  |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth | J2B, J3E, H3E, F1B |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 400 W (1605-4000 kHz) Maximum 1500 W (4000-27500kHz) |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to GMDSS radio operator certificate, radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions | EN 300 373 |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 300 373, EN 303 402, EN 300 338, ETS 300 067, SOLAS, ITU-R, IMO, EN 301 843-1 (EMC), EN 301 843-2 (EMC), EN 62368-1 (LVD). | . |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | EPIRBs | TAD06-01-03 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime Mobile Satellite |  |
|  | 2 | Application | EPIRBs | GMDSS / COSPAS-SARSAT |
|  | 3 | Frequency band | A: 121.45 - 121.55 MHz B: 242.95 - 243.05 MHz C: 406.00 - 406.10 MHz | 121.5 MHz 243.0 MHz 406.0 MHz |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth |  |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 5 W e.i.r.p. (406 MHz) Maximum 100 mW e.i.r.p. (121.5 MHz, 243 MHz) |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions |  |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 300 066, SOLAS, ITU-R, IMO, EN 301 843-1 (EMC), EN 301 843-2 (EMC), EN 62368-1 (LVD) |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | AIS | TAD06-01-04 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime Mobile | Automatic Identification System |
|  | 2 | Application | AIS | AIS |
|  | 3 | Frequency band | 161.9625-161.9875 MHz 162.0125-162.0375 MHz |  |
|  | 4 | Channelling | 12.5 kHz, 25 kHz |  |
|  | 5 | Modulation / Occupied bandwidth | GMSK / FM |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 25 W |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements | 2005/53/EC |  |
|  | 11 | Frequency planning assumptions |  |  |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | ERC/DEC/(99)17, SOLAS, ITU-R Rec. M.1371-1, EN 301 843-1 (EMC), EN 301 843-2 (EMC), EN 62368-1 (LVD). |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Maritime Radar | TAD06-01-05 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime |  |
|  | 2 | Application | Maritime Radar | Maritime Radar |
|  | 3 | Frequency band | 9300 - 9500 MHz |  |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth | PON |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 10 kW transmitter power Maksimum 10 MW e.i.r.p. |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions | EN 302 194-1 | ITU-RR APP.3 ITU-R M.1177, ITU-R SM.1541, ERC/REC 74-01. |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 302 194-2, ERC/REC 74-01, EN 301 843-1 (EMC), EN 301 843-2 (EMC), 62368-1 (LVD). |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |

| Republic of Turkey Information and Communications Technologies Authority | Radio Interface Specification | Maritime Radar | TAD06-01-06 |  |
| --- | --- | --- | --- | --- |

|  | Nr | Parameter | Description | Comments |
| --- | --- | --- | --- | --- |
| Normative Part | 1 | Radiocommunication Service | Maritime |  |
|  | 2 | Application | Maritime Radar | Maritime Radar (non-SOLAS) |
|  | 3 | Frequency band | 9300 - 9500 MHz |  |
|  | 4 | Channelling |  |  |
|  | 5 | Modulation / Occupied bandwidth | PON |  |
|  | 6 | Direction / Separation |  |  |
|  | 7 | Transmit power / Power density | Maximum 25 kW transmitter power Maksimum 50 MW e.i.r.p. |  |
|  | 8 | Channel access and occupation rules |  |  |
|  | 9 | Authorisation regime | Subject to radio license and permission to install and use the radio equipment (General Directorate of Coastal Safety). |  |
|  | 10 | Additional essential requirements |  |  |
|  | 11 | Frequency planning assumptions | EN 302 248 | ITU-RR APP.3, ITU-R M.1177, ITU-R SM.329, ITU-R SM.1541, ERC/REC 74-01. |
| Informative Part | 12 | Planned changes |  |  |
|  | 13 | Reference | EN 302 248, ERC/REC 74-01, EN 301 843-1 (EMC), EN 301 843-2 (EMC), EN 62368-1 (LVD). |  |
|  | 14 | Notification number |  |  |
|  | 15 | Remarks |  |  |